The documentation of the tools for V3 energy meters

SHENZHEN CONSTANT ELECTRONICS COMPANYLIMITED

Tel: 0755-89748618

Fax: 0755-89748618

Email: wangjg@vip.163.com

Web：www.cstdevice.com

# 1General

This file is to explain how apply the tools for V3 energy meters. We design the tools for operating the V3 energy meters on site; therefore they are the effective supplement to V3 centralized measurement system.

These tools can be divided into two categories: Modems and Converters. Modem is function to modulation/demodulation between air RF signal and communication text, default applies RF signal protocol (private agreement). For a converter, it not only modulate/demodulate RF signal, but also convert the communication protocol between DL/T645 and RF signal agreement. That is not to say converter more powerful, on site different application case require different type tool. Normally user by HHU (or cell phone) and the modem operate V3 energy meters, read meter data or control built-in relay connection/disconnection. Engineer can also supervise the communication text by the modem, by which behavior he can find the error on site. The Converter usually play a role of concentrator to control a individual V3 energy meter, this way can save cost. Under this case, a DCU (data communication unit) link with public net for remotely communication with Power Utility; DCU connect the Converter by RS232 interface, Converter bridges communication between V3 energy meter and DCU.

# 2 Specifications

## 2.1 function list

| Name | Type | RF Channel | Interface | Connection | Apply to |
| --- | --- | --- | --- | --- | --- |
| V3 modem of RS232 version | LDAG19A | LORA + BBS | RS232 | HHU or computer | LORA meter and BBS meter on site |
| V3 modem of BT version | LDAG20A | LORA + BBS | Bluetooth | cell phone | LORA meter and BBS meter on site |
| LORA MODEM | LDAG17A | LORA | RS232 | HHU or computer | LORA meter on site |
| BBS MODEM | LDAG18A | BBS | RS232 | HHU or computer | BBS meter on site |
| LORA CONVERTER | LDAG21A | LORA | RS232 | DCU(GPRS Modem) | remotely operate LORA meter |

## 2.2 power supply

| Type | Power position | Power voltage (DC) | Power consumption | Annex | Input of power supply |
| --- | --- | --- | --- | --- | --- |
| LDAG19A | Side socket | 7-12V | 250mA | power supply | 90--240V AC |
| LDAG20A | Bottom USB socket | 5V | 250mA | USB power wire | No applicable |
| LDAG17A | Side socket | 7-12V | 220mA | power supply | 90--240V AC |
| LDAG18A | Side socket | 7-12V | 50mA | power supply | 90--240V AC |
| LDAG21A | Side socket | 7-12V | 220mA | power supply | 90--240V AC |

## 2.3 communication parameter

| Type | RF frequency | Effective distance | Protocol | Encryption | bps |
| --- | --- | --- | --- | --- | --- |
| LDAG19A | 915M/2.4G | 300m/3m | LOAR/BBS | applicable | 9.3k/1M |
| LDAG20A | 915M/2.4G | 300m/3m | LOAR/BBS | applicable | 9.3k/1M |
| LDAG17A | 915M | 300m | LORA | No applicable | 9.3K |
| LDAG18A | 2.4G | 3m | BBS | No applicable | 1M |
| LDAG21A | 915M | 300m | DL/T645 | No applicable | 9.3K |

# 3 Applications

## 3.1 the structure of the tools with RS232 interface

## 3.2 the structure of the tools with Bluetooth interface

## 3.3 connection1

The follow diagram shows the connection for the tools with RS232 interface, on site when application.

## 3.4 connection2

The follow diagram shows the connection for the tools with BT interface, on site when application.

# 4 Declarations

Manufacture reserves the all rights of the products of explain， modification and version upgrade, and don’t duty to announce users when there are some changes above. Manufacture is only responsible for the products themselves, don’t duty to any other behaviors as use or install the products lead to.